## Slide 1: 3) MIPS 분기 명령어 (section 2.7)
분기 명령어 = branch instructions
  jr $31 # jump register
  j L1 # jump
  jal L1 # jump and link
  beq $2, $3, L1 # branch equal
  bne $4, $5, L1 # branch not equal
§2.7 Instructions for Making Decisions

## Slide 2: Control flow of a program
a program = a sequence of instructions
명령어들은 순서대로 실행된다. (except branch instructions)
Loop: add $2, $3, $2
addi $4, $5, 10
sub $8, $7, $6
bne $11, $12, Exit
lw $13, 0($14)
j Loop
Exit: subi $2, $4, $0
Labels are used in branch instr.

## Slide 3: Labels in assembly code
MIPS 명령어들은 32bits 의 이진수로 표현되어 메모리에 저장된다.
각 명령어의 메모리 주소는 32bits 숫자로 표현된다.
그러나 Assembly code 에서는 숫자로 된 명령어 주소를 알 수 없다.
Assembly code 에서는 기호로 된 Label 을 명령어 앞에 써서 숫자로 된 명령어 주소 대신 사용한다.
Label 은 알파벳과 숫자로 구성된 식별자를 사용한다. 첫글자는 숫자가 될 수 없다. (high-level language 에서 변수를 만드는 것과 비슷함)
Label 은 assembler/linker 가 나중에 실제 주소로 바꾸어 준다.
(Label 이 왜 필요할까?)
Loop: add $2, $3, $4 # Loop is Label

## Slide 4: Unconditional Branch jr/j/jal
jr $31 # jump register
  unconditional jump to instruction stored in R[$31]
j L1 # jump
  unconditional jump to instruction labeled L1
jal L1 # jump and link
  unconditional jump to instruction labeled L1
  and store the next address in $31 ($ra : return address)
§2.7 Instructions for Making Decisions

## Slide 5
.text
.globl main
main:
nop
la $t1, main
jr $t1
BTA : Branch (Jump) Target Address
jr instruction

## Slide 6
main = 0x00400024

## Slide 7
assembler temporary

## Slide 9
Program Counter

## Slide 10
.text
.globl main
main:
nop
la $t1, main
jr $t1
0x01200008 (R format)
= 0000 0001 0010 0000 0000 0000 0000 1000
= 000000 01001 00000 00000 00000 001000
op rs rt rd shamt ftn
BTA : Branch (Jump) Target Address = 0x00400024
Representation of jr
0000 0000 0100 0000 0000 0000 0010 0100
$t1

## Slide 11: MIPS opcode map
Appendix A-50

## Slide 12
.text
.globl main
main:
nop
j main
BTA : Branch (Jump) Target Address
j instruction

## Slide 15
.text
.globl main
main:
nop
j main
0x08100009
= 0000 1000 0001 0000 0000 0000 0000 1001
000010 00 0001 0000 0000 0000 0000 1001
j 명령어의 BTA 를 계산하는 법 :
0000 00 0001 0000 0000 0000 0000 1001 00
PC 의 상위 4 bits (j 명령 수행 시 PC 의 값 = 0x00400028)
BTA : Branch (Jump) Target Address = 0x00400024
Representation of j : J format
무조건 00 으로 채운다.
명령어의 주소는
4의 배수이므로

## Slide 16: MIPS opcode map
Appendix A-50

## Slide 17
.text
.globl main
main:
nop
jal main
nop # return address
BTA : Branch (Jump) Target Address
jal instruction

## Slide 18
.text
.globl main
main: addi $a1, $0, 1
jal foo
lui $t0, 0x1001 # return address
sw $a0, 0($t0)
foo: add $a0, $a1, $a1
jr $ra # end of subroutine (return)
0x0c10000d
= 0000 1100 0001 0000 0000 0000 0000 1101
000011 00 0001 0000 0000 0000 0000 1101
J format명령어의 BTA 를 계산하는 법 :
0000 00 0001 0000 0000 0000 0000 1101 00
PC 의 상위 4 bits (jal 명령 수행 시 PC 의 값 = 0x00400028)
BTA : = 0x00400034
Representation of jal : J format
무조건 00 으로 채운다.
명령어의 주소는
4의 배수이므로
RA : = 0x0040002C

## Slide 20
Return Address Register

## Slide 25: MIPS opcode map
Appendix A-50

## Slide 26: Conditional Branch beq/bne
beq $rs, $rt, L1 # branch equal
  rs 레지스터의 32bits 값이 rt 레지스터의 32bits 값과 같으면 L1 이 가리키는 명령어를 수행
  if (R[$rs] == R[$rt]) branch to instruction labeled L1
  아니면 다음 명령어를 수행
bne rs, rt, L1 # branch not equal
  if (R[$rs] != $R[$rt]) branch to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 27: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
f = 2*f;
Compiled MIPS code:
  가정: f in $s0, g in $s1, h in $s2, i in $s3, j in $s4
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: add $s0, $s0, $s0
Labels : Assembler calculates memory addresses of these labels

## Slide 31
if ( i==j)

## Slide 37
0x16740003
= 0001 0110 0111 0100 0000 0000 0000 0011
000101 10011 10100 0000 0000 0000 0011
bne/neq 명령어의 BTA 를 계산하는 법 :
PC 의 값 + 명령어의 immediate field (sign-extended) x 4
0000 0000 0100 0000 0000 0000 0011 1000
+ ???? ???? ???? ??00 0000 0000 0000 1100
0000 0000 0100 0000 0000 0000 0100 0100
BTA : Branch (Jump) Target Address = 0x00400044
Representation of bne : I format
x4
bne 수행 시 PC 의 값
= 0x00400038

## Slide 38: MIPS opcode map
Appendix A-50

## Slide 39: Why BTA calculation?
BTA 는 branch instruction 에 local 하기 때문

## Slide 40: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
beq $s0,$s1, L1
add …
…
L1: sub … # far away
  bne $s0,$s1, L2 j L1
  L2: add …
  …
  L1: sub … # far away
=