## Slide 1: Set-if-Less-Than (slt) instruction
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (R[$rs] < R[$rt]) R[$rd] = 1; else R[$rd] = 0;
slti rd, rs, constant
  if (R[$rs] < constant) R[$rd] = 1; else R[$rd] = 0;
Use in combination with beq, bne
  slt $s0, $s3, $s4 # if (R[$s3] < R[$s4]) bne $s0, $zero, Target # branch to Target

## Slide 5: Signed vs. Unsigned slt
Signed comparison: slt, slti
Unsigned comparison: sltu, sltiu
Example
  $s3 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s4 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $s0, $s3, $s4 # signed
    –1 < +1 Þ R[$s0] = 1
  sltu $s0, $s3, $s4 # unsigned
    +4,294,967,295 > +1 Þ R[$s0] = 0

## Slide 9: blt : pseudoinstruction
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 12: slt/sltu : R-format instruction
slt $16, $19, $20
000000 10011 10100 10000 00000 101010
0000 0010 0111 0100 1000 0000 0010 1010
= 0x0274802A

## Slide 13: MIPS opcode map
Appendix A-50

## Slide 14: slti/sltiu : I-format instruction
slti $16, $19, 0
001010 10011 10000 0000000000000000
0010 1010 0111 0000 0000 0000 0000 0000
= 0x2A700000
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 15: Compiling Loop Statements
C code:
i = 1;
while (arr[i] == k) i++;
  i in $s3, k in $s5, address of arr in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 # $t1 = 4*i add $t1, $t1, $s6 # $t1 = &arr[i] lw $t0, 0($t1) # $t0 = arr[i] bne $t0, $s5, Exit addi $s3, $s3, 1 # i++ j Loop Exit: …

## Slide 31: Branch example
bne $2,$3,L1 [0x0040 0024] 000101 00010 00011 0000 0000 0000 0010
add $4,$5,$6 [0x0040 0028] 000000 00101 00110 00100 00000 100000
L1: lw $7,4($16) [0x0040 002C] 100011 10000 00111 0000 0000 0000 0100
L2: sw $7,-4($16) [0x0040 0030] 101011 10000 00111 1111 1111 1111 1100
j L3 [0x0040 0034] 000010 00 0001 0000 0000 0000 0001 0000
beq $2,$3,L2 [0x0040 0038] 000100 00010 00011 1111 1111 1111 1110
sub $6,$4,$5 [0x0040 003C] 000000 00100 00101 00110 00000 100010
L3: [0x0040 0040]
L1 from bne : 0000 0000 0100 0000 0000 0000 0010 0100
+ ???? ???? ???? ??00 0000 0000 0000 1000 (?=0)
0000 0000 0100 0000 0000 0000 0010 1100
L3 from j : 0000 00 0001 0000 0000 0000 0001 0000 00 4의 배수
L2 from beq : 0000 0000 0100 0000 0000 0000 0011 1000
+ ???? ???? ???? ??11 1111 1111 1111 1000 (?=1)
0000 0000 0100 0000 0000 0000 0011 0000
Memory addresses
Memory contents

## Slide 35: Representing Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4!= $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Instruction Formats:
Addresses are not 32 bits hint: How did we handle this with load and store instructions?
op rs rt 16 bit address
op 26 bit address
I
J

## Slide 36: Representing Branch Target Address
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4!=t5
  beq $t4,$t5,Label Next instruction is at Label if $t4=$t5
Instruction Formats:
Could specify a register (like lw and sw) and add it to address
  use Instruction Address Register (PC = program counter)
  most branches are local (principle of locality)
  address offsets are always multiples of 4
  Branch Target Address of bne,beq instruction = ($PC) + 4 x offset
Jump instructions just use high order bits of PC
  address boundaries of 256 MB
  Branch Target Address of j instruction = PC(31:28) | 4 x offset
op rs rt 16 bit address
I

## Slide 37: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time

## Slide 38: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 39: 2.9 Addressing Mode Summary

## Slide 40: Summary of basic instructions
Instruction Meaning add $s1,$s2,$s3 $s1 = $s2 + $s3 sub $s1,$s2,$s3 $s1 = $s2 - $s3 lw $s1,100($s2) $s1 = Memory[$s2+100] sw $s1,100($s2) Memory[$s2+100] = $s1 bne $s4,$s5,L Next instr. is at Label if $s4 !=$s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
3 MIPS Instruction Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 41: HW3 : due 10/7 Monday 11:00AM
다음의 프로그램을 작성하여 SPIM 에 로드하여 실행해 보고
프로그램이 하는 일을 c 언어로 표현하라.
nop 를 제외한 명령어 12개를 모두 2진수로 표현하고 R,I,J format 중 어느 format 인지 설명하고 field 별로 나누어 그 의미를 설명하라. (MIPS opcode map 참조)
숙제 제출은 ecampus 에 직접 작성으로 에디터에 작성하되 그림 파일은 절대로 첨부하지 말 것. (그림 첨부 시 0점 처리)

## Slide 42
.data 0x10010000
a:
.word 30
.word 50
.word -10
.word 45
.word 100
.text
.globl main
main: lui $s0, 0x1001
addi $s1, $0, 5
add $t0, $0, $0
add $s2, $0, $0
for: slt $t1, $t0, $s1
beq $t1, $0, end
lw $t2, 0($s0)
add $s2, $s2, $t2
addi $t0, $t0, 1
addi $s0, $s0, 4
j for
end: nop
jr $ra

## Slide 43: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 44: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Program is a sequence of instructions
Processor fetches and executes instructions from memory in sequence.
The BIG Picture