## Slide 1: 중간고사 10/22 화요일 아침 9시 – 10시

## Slide 2: 2.8 Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware

## Slide 3: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements

## Slide 4: Handling a Procedure Call
jal & jr commands are used in pairs.
Example : ultimately simple example
main procedure subroutine
.text
.globl main
main: .
.
.
.
jal foo
.
.
.text
.globl foo
foo: .
.
.
.
jr $ra

## Slide 5: Policy of MIPS Register Use Conventions
How to pass arguments and return values in function call

## Slide 6: Register Usage in function call
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 7: System Calls : calls to functions implemented in OS
Example : addi $v0, $0, 1 # system call code
addi $a0, $0, 10 # argument for the system call, if necessary
syscall

## Slide 9: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 11: 다른 함수를 호출하지 않는 함수라면
C code:
int leaf_example (int g, h, i, j){
int f;
f = (g + h) - (i + j); return f; }
  Arguments g,h,i,j in $a0, $a1, $a2, $a3
  f in $s0
  $s0, $t0, $t1 will be saved on stack.
  Result in $v0

## Slide 12: Leaf Procedure Example
Save $t0,$t1,$s0 on stack
Procedure body
Restore $t0,$t1,$s0 from stack
Return value in $v0
Return to caller function
leaf_example: addi $sp, $sp, -12
sw $t1, 8($sp)
sw $t0, 4($sp)
sw $s0, 0($sp) add $t0, $a0, $a1 # g+h add $t1, $a2, $a3 # i+j sub $s0, $t0, $t1 # f add $v0, $s0, $zero lw $s0, 0($sp)
lw $t0, 4($sp)
lw $t1, 8($sp) addi $sp, $sp, 12 jr $ra

## Slide 13
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 2.10 The values of the stack pointer and the stack (a) before, (b) during, and (c) after the procedure call. The stack pointer always points to the “top” of the stack, or the last word in the stack in this drawing.

## Slide 14: Why? Caller function
$t0,$t1,$s0 used in caller
set up function arguments
print return value
using system call
function call
print some value
based on values of $t0, $t1:
what happens if these are
not saved?
main: addi $t0, $0, 100
addi $t1, $0, 200
addi $s0, $0, 300
addi $a0, $0, 4 # g
addi $a1, $0, 3 # h
addi $a2, $0, 1 # i
addi $a3, $0, 2 # j
jal leaf_example add $a0, $v0, $0
addi $v0, $0, 1
syscall
add $a0, $t1, $t0 syscall

## Slide 19
8($sp)

## Slide 21
4($sp)

## Slide 23
0($sp)

## Slide 33: Why stack? 함수가 다른 함수를 호출한다면
Procedure call/returns are Last-In-First-Out
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call
Our Example :
  SPIM startup code -> main -> leaf_example

## Slide 34: Non-Leaf Example : main
Save registers
including $ra on stack
set up arguments
Restore registers
including $ra from stack
Return to caller
function call
print return value
using system call
main: addi $sp, $sp, -24 # main: (non_leaf example)
sw $ra, 0($sp)
sw $a0, 4($sp)
sw $a1, 8($sp)
sw $a2, 12($sp)
sw $a3, 16($sp)
sw $v0, 20($sp)
addi $a0, $0, 4 # g
addi $a1, $0, 3 # h
addi $a2, $0, 1 # i
addi $a3, $0, 2 # j
jal leaf_example # leaf_example(g,h,i,j)
add $a0, $v0, $0 # $a0 <= return value
addi $v0, $0, 1
syscall # print return value
lw $ra, 0($sp)
lw $a0, 4($sp)
lw $a1, 8($sp)
lw $a2, 12($sp)
lw $a3, 16($sp)
lw $v0, 20($sp)
addi $sp, $sp, 24
jr $ra

## Slide 35
SPIM startup code calls main

## Slide 37
old stack top

## Slide 40
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
stack
$sp =7ffffdd8 
$sp = 7ffffdc0 
00000003

## Slide 44
old stack top

## Slide 46
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
stack
$sp = 7ffffdb4 
00000000
00000000
00000000
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
$sp = 7ffffdc0 

## Slide 51
00000000
00000000
00000000
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
stack
$sp = 7ffffdb4 
00000000
00000000
00000000
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
$sp = 7ffffdc0 

## Slide 58
00000000
00000000
00000000
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
stack
$sp = 7ffffdd8 
00000000
00000000
00000000
00400018
00000003
7FFFFDDC
7FFFFDEC
00000000
0000000C
00000003
$sp = 7ffffdc0 

## Slide 61: Stack 에는 함수의 지역 변수도 저장된다.
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 62: Recursive Procedure Example
C code:
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 63: Recursive Procedure
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 64: recursive call to fact with $a0=2
main : addi $a0, $0, 2
jal fact
ret: nop
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call L2: lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
$a0=
2 1 0
$sp
$sp
$sp
$sp
stack

## Slide 65: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 66: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: describes contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 67: Linking Object Modules (Static)
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 68
Copyright © 2014 Elsevier Inc. All rights reserved.

## Slide 69
Copyright © 2014 Elsevier Inc. All rights reserved.
R[$gp] 0x10008000
+ 0x????8000 (? = 0xF, due to sign extention)
= 0x10000000
extern in C, .globl in MIPS assembly 가 symbol 의 외부 참조를 가능하게 함
B:
A:

## Slide 70: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 71: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 72: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code