## Slide 1: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Infinite loads:
  Speedup = 4n/(3+n) ≈ 4 = number of stages

## Slide 2: Datapath With Control

## Slide 3: Pipelining 을 하려면
load 를 여러 개의 sub-task 로 나누어야 함
각 sub-task 는 1-clock cycle 에 수행된다.

## Slide 4: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 5: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 6: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 7: tesseract from movie “interstellar”(2014)

## Slide 8: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 9: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle (CC5)

## Slide 10: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 11: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 12: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 13: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 14: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 15: Single-Cycle Pipeline Diagram
State of pipeline in CC5

## Slide 16: IF for Load at CC1

## Slide 17: ID for Load at CC2

## Slide 18: EX for Load at CC3

## Slide 19: MEM for Load at CC4

## Slide 20: WB for Load at CC5
Wrong register number

## Slide 21: Corrected Datapath for Load

## Slide 22: EX for Store

## Slide 23: MEM for Store

## Slide 24: WB for Store

## Slide 25: Single-Cycle Pipeline Diagram
State of pipeline at CC5

## Slide 26: Pipelined Control (Simplified)

## Slide 27: Control Signals

## Slide 28: Control Signals

## Slide 29: Truth Table for Pipeline Control

## Slide 30: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 31: Pipelined Control