## Slide 1: Chapter 2
Instructions : Language of the Computer

## Slide 2: Representation of a Program
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 3
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.
000000100011001001000000001000002
17번 방의 값과
18번 방의 값을
더해서 8번 방에 써라.

## Slide 4
Logic Diagram of a Processor

## Slide 5
5
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.8 The logic board of Apple iPad 2 in Figure 1.7. The photo highlights five integrated circuits. The large integrated circuit in the middle is the Apple A5 chip, which contains a dual ARM processor cores that run at 1 GHz as well as 512 MB of main memory inside the package. Figure 1.9 shows a photograph of the processor chip inside the A5 package. The similar sized chip to the left is the 32 GB flash memory chip for non-volatile storage. There is an empty space between the two chips where a second flash chip can be installed to double storage capacity of the iPad. The chips to the right of the A5 include power controller and I/O controller chips. (Courtesy iFixit, www.ifixit.com)
inside iPad 2

## Slide 6: Instruction Set Architecture (ISA)
컴퓨터 (프로세서) 에서 사용되는 명령어들의 집합 및 그 정의
Different computers (processors) have different ISAs
  But with many aspects in common
Many modern computers have simple instruction sets
그 중에서 MIPS ISA 를 배울 것임.
§2.1 Introduction

## Slide 7: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendix A.10

## Slide 9: Types of Instructions
Arithmetic / Logic instructions 연산 명령어
= ALU operations
Data transfer instructions 메모리 접근 명령어
= Load/Store instructions
Branch instructions 분기 명령어
= Control transfer instructions

## Slide 10
1. MIPS
Arithmetic Instructions

## Slide 11: 1) MIPS Arithmetic Instructions
덧셈, 뺄셈, 곱셈, 나눗셈 등의 산술 논리 연산 명령어들
add a, b, c # a gets b + c
operation source operands
destination operand comments
§2.2 Operations of the Computer Hardware
instruction

## Slide 12: MIPS Arithmetic
C code:
f = g + h;
Compiled MIPS code:
add f, g, h # f = g + h

## Slide 13: Operands of Arithmetic Instructions
3 operands : 1 destination, 2 sources
Arithmetic instructions use only register operands
§2.3 Operands of the Computer Hardware

## Slide 14: Registers
레지스터 : 프로세서 내부에 있는, 작고 빠른 임시의 메모리
MIPS has a 32 × 32-bit register file ($0 ~ $31)
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Design Principle : Smaller is faster
  c.f. main memory: millions of locations

## Slide 15
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.
register
Registers vs. Memory

## Slide 16: MIPS Arithmetic Instructions : revisited
add a, b, c # a gets b + c
operation source operands
destination operand comments
§2.2 Operations of the Computer Hardware

## Slide 17: MIPS Arithmetic
C code:
f = g + h;
Compiled MIPS code:
add $3, $4, $5

## Slide 18: MIPS Arithmetic
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
(가정: f in $2, g in $3, h in $4, i in $5, j in $6)
add $7, $3, $4 # $7 = g + h add $8, $5, $6 # $8 = i + j sub $2, $7, $8 # f = $7 - $8

## Slide 19
1-1. MIPS
Immediate Arithmetic/Logic Instructions

## Slide 20: MIPS Immediate Arithmetic Instructions
C code:
f = g + 10;
Compiled MIPS code:
(가정: f in $2, g in $3)
addi $2, $3, 10 # 3rd operand 만 상수

## Slide 21: The Constant Zero
MIPS register 0 ($zero or $0) 의 값은 항상 0 이다.
  바뀌지 않는다.
Useful for common operations
  E.g., move between registers
  add $5, $4, $zero

## Slide 22: Exercise
.text
.globl main
main:
addi $8, $0, 10 # Q1 : 이 명령어를 실행한 후 8번 레지스터의 값은 얼마인가? (십진수과 16진수로 쓰시오.)
addi $9, $0, 16 # Q2 : 이 명령어를 실행한 후 9번 레지스터의 값은 얼마인가? (십진수과 16진수로 쓰시오.)
add $10, $8, $9 # Q3 : 이 명령어를 실행한 후 10번 레지스터의 값은 얼마인가? (십진수과 16진수로 쓰시오.)
십진수 10을 32bit 16진수로 쓰면 0x0000 000A
이진수로는 0000 0000 0000 0000 0000 0000 0000 1010
* 십진수 16을 32bit 16진수로 쓰면 0x0000 0010
이진수로는 0000 0000 0000 0000 0000 0000 0001 0000

## Slide 23: Hexadecimal Numbers (16진수)
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: 0xeca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 25: MIPS Register Aliases