## Slide 1
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.
register
000000000000000000000000000000002

## Slide 2
000000000000000000000000000000002
Store
Load

## Slide 4: 2) MIPS Data Transfer Operations
store instruction : register -> memory
sw $4, 8($5)
“store word” offset
operation memory address = R[$5] + 8
source operand in register
§2.2 Operations of the Computer Hardware
base register

## Slide 5
load instruction : memory -> register
lw $4, 8($5)
“load word” offset
operation memory address = R[$5] + 8
destination operand in register
§2.2 Operations of the Computer Hardware
base register

## Slide 6: 다음 코드 수행 결과 $4, $5, $6 의 값은?
.text
.globl main
main:
lui $5, 0x1000
lui $4, 0x789A
ori $4, $4, 0xBCDE
sw $4, 8($5)
lw $6, 8($5)

## Slide 9
[0x10000008]

## Slide 11: Representing data transfer instructions
sw $4, 8($5)
lw $4, 8($5)

## Slide 12: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 ~ (+215 – 1)
  Address: offset added to base address stored in rs register
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 13: MIPS opcode map
Appendix A-50

## Slide 14: sw $4, 8($5)
1010 1100 1010 0100 0000 0000 0000 1000
= 0xaca40008
101011
00101
00100
0000 0000 0000 1000
6 bits
5 bits
5 bits
16 bits

## Slide 16: dissassemble 0x8ca60008
=1000 1100 1010 0110 0000 0000 0000 1000
lw $4, 8($5)
100011
00101
00110
0000 0000 0000 1000
6 bits
5 bits
5 bits
16 bits

## Slide 17: MIPS assembler features
Comments
Labels
Numbers are base 10, Hexadecimals are prefixed with 0x
Strings are enclosed with “ and “
Special characters : \n, \t and \”
Assembler directives :
  .ascii, .asciiz “some string”
  .space n
  .byte, .half, .word, .float, .double d1, d2, … dn
  .data <addr>
  .text <addr>
  .globl symbol

## Slide 18: Initializing Data Segment
.data
.byte 1
.byte -2
.space 3
.byte ‘s’
in C,
char a[] = {1,-2, 0, 0, 0, 0x73};
// 0x73 는 ‘s’ 의 ASCII code
0x01
0xfe
0x00
0x00
0x00
0x73
[0x10010000]
[0x10010001]
[0x10010002]
[0x10010003]
[0x10010004]
[0x10010005]

## Slide 19: Initializing Data Segment
.data 0x10020000
w1: .word 1
.word -1
.word 0xabcdef12
.word 0xffff
.text
.globl main
main : lui $5, 0x1002
lui $4, 0x789a
sw $4, 8($5)
in C,
int w1[4] = {1,-1, 0xabcdef12, 0xffff} ;
int main(){
w1[2] = 0x789a0000;
}
[0x10020000]
[0x10020001]
[0x10020002]
[0x10020003]
[0x10020004]
[0x10020005]
[0x10020006]
[0x10020007]
[0x10020008]
[0x10020009]
[0x1002000a]
[0x1002000b]
[0x1002000c]
[0x1002000d]
[0x1002000e]
[0x1002000f]
label
0x00000001
0xffffffff
0xabcdef12
0x0000ffff

## Slide 23: Initializing Data Segment
.data 0x10030000
str1: .byte ‘s’
.byte ‘t’
.byte ‘a’
.byte ‘r’
.byte 0
str2: .ascii “star”
str3:
.asciiz “star”
in C,
char str1[] = {‘s’,’t’,’a’,’r’,’\0’};
char str2[] = {‘s’,’t’,’a’,’r’};
char str3[] = “star”; // = {‘s’,’t’,’a’,’r’,’\0’};
0x73
0x74
0x61
0x72
0x00
0x73
0x74
0x61
0x72
0x73
0x74
0x61
0x72
0x00
[0x10030000]
[0x10030001]
[0x10030002]
[0x10030003]
[0x10030004]
[0x10030005]
[0x10030006]
[0x10030007]
[0x10030008]
[0x10030009]
[0x1003000a]
[0x1003000b]
[0x1003000c]
[0x1003000d]

## Slide 24: 글자를 모아 단어를 만들 때
한국어,영어는 왼쪽에서 오른쪽으로 쓴다.
STAR
아랍어는 오른쪽에서 왼쪽으로 쓴다.
왜? 규칙이니까.

## Slide 25: 4개의 byte 를 모아 word 를 만들 때도 2가지 방향이 가능
0x00000001
0xffffffff
0xabcdef12
0x0000ffff
[0x10020000]
[0x10020001]
[0x10020002]
[0x10020003]
[0x10020004]
[0x10020005]
[0x10020006]
[0x10020007]
[0x10020008]
[0x10020009]
[0x1002000a]
[0x1002000b]
[0x1002000c]
[0x1002000d]
[0x1002000e]
[0x1002000f]
0xab
0xcd
0xef
0x12
0x12
0xef
0xcd
0xab
Little endian
byte order
big endian
byte order

## Slide 26: Byte order : Little endian vs. Big endian
.data 0x10010000
.byte 1
.byte 2
.byte 3
.byte 4
Little endian : intel
Big endian : SPARC, Motorola
MIPS : can be configured to either one
[10010000]
[10010001]
[10010002]
[10010003]
0x01
0x02
0x03
0x04
a word at 10010000 = 0x04030201
a word at 10010000 = 0x01020304

## Slide 27: 0x10010000 ~ 0x10010003 에 저장된 내용을 word 로 읽으면?
.data
.byte 1
.byte -2
.space 3
.byte ‘s’
in C,
char a[] = {1,-2, 0, 0, 0, 0x73};
// 0x73 는 ‘s’ 의 ASCII code
0x01
0xfe
0x00
0x00
0x00
0x73
[0x10010000]
[0x10010001]
[0x10010002]
[0x10010003]
[0x10010004]
[0x10010005]
0x01fe0000 ?
(big endian)
0x0000fe01 ?
(little endian)

## Slide 28: SPIM 에서 memory 내용을 보여줄 때 word 단위로 보여줌

## Slide 29: Little endian byte order
.data 0x10020000
w1: .word 1
.word -1
.word 0xabcdef12
.word 0xffff
.text
.globl main
main : lui $5, 0x1002
lui $4, 0x789a
sw $4, 8($5)
in C,
int w1[4] = {1,-1, 0xabcdef12, 0xffff} ;
int main(){
w1[2] = 0x789a0000;
}
[0x10020000]
[0x10020001]
[0x10020002]
[0x10020003]
[0x10020004]
[0x10020005]
[0x10020006]
[0x10020007]
[0x10020008]
[0x10020009]
[0x1002000a]
[0x1002000b]
[0x1002000c]
[0x1002000d]
[0x1002000e]
[0x1002000f]
label
0x00000001
0xffffffff
0xabcdef12
0x0000ffff
0x01
0x00
0x00
0x00
0xff
0xff
0xff
0xff
0x12
0xef
0xcd
0xab
0xff
0xff
0x00
0x00

## Slide 31
.data 0x10030000
str1: .byte ‘s’
.byte ‘t’
.byte ‘a’
.byte ‘r’
.byte 0
str2: .ascii “star”
str3:
.asciiz “star”
in C,
char str1[] = {‘s’,’t’,’a’,’r’,’\0’};
char str2[] = {‘s’,’t’,’a’,’r’};
char str3[] = “star”; // = {‘s’,’t’,’a’,’r’,’\0’};
0x73
0x74
0x61
0x72
0x00
0x73
0x74
0x61
0x72
0x73
0x74
0x61
0x72
0x00
[0x10030000]
[0x10030001]
[0x10030002]
[0x10030003]
[0x10030004]
[0x10030005]
[0x10030006]
[0x10030007]
[0x10030008]
[0x10030009]
[0x1003000a]
[0x1003000b]
[0x1003000c]
[0x1003000d]
0x72617473
0x61747300
0x61747372

## Slide 32: SPIM 에서 이 부분은 byte 단위로 보여줌

## Slide 33: word alignment
.data 0x10010000
a: # 0x10010000
.byte 1
.byte -2
.space 3
.byte 's' # 0x10010005
w1: # 0x10010008
.word 1
.word -1
.word 0xabcdfe12
.word 0xffff
.text
.globl main
main:
la $5, a # pseudoinstruction
la $6, w1
lw $4, 0($6)
0x01
0xfe
0x00
0x00
0x00
0x73
0x01
0x00
0x00
0x00
[0x10010000]
[0x10010001]
[0x10010002]
[0x10010003]
[0x10010004]
[0x10010005]
[0x10010006]
[0x10010007]
[0x10010008]
[0x10010009]
[0x1001000a]
[0x1001000b]
[0x1001000c]
[0x1001000d]
[0x1001000e]
[0x1001000f]
0x00000001
for word alignment

## Slide 35: la (load address) pseudoinstruction 에서 label 의 사용

## Slide 38: Memory Operands
변수들은 Main memory 에 저장됨
  Arrays, structures, dynamic data
산술 연산을 하려면
  메모리에 있는 변수 값을 먼저 레지스터로 Load
  연산을 수행
  레지스터에 있는 연산 결과를 메모리에 Store
Memory is byte addressed
  8-bit byte 마다 주소가 있음
Words (= 4 bytes) are aligned in memory
  워드 주소는 4의 배수
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 39: Byte addressing
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 2.3 Actual MIPS memory addresses and contents of memory for those words. The changed addresses are highlighted to contrast with Figure 2.2. Since MIPS addresses each byte, word addresses are multiples of 4: there are 4 bytes in a word.
4bytes

## Slide 40: Memory Operand Example 1
C code:
int g,h,A[100];
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 41: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
23
$s3
$s2
1032
1048
1000
3
$t0
?
20
memory
processor
A[8]
A[12]
h
&A[0]

## Slide 42: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Program is a sequence of instructions
Processor fetches and executes instructions from memory in sequence.
The BIG Picture