## Slide 1: Chapter 4
The Processor

## Slide 2
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.

## Slide 3: In this chapter,
We will examine two MIPS implementations in logic gate level.
  first, a simplified version
  second, a more realistic pipelined version
Our implementation will execute a simple subset of MIPS instructions.
  Memory reference instructions: lw, sw
  Arithmetic/logical instructions: add, sub, and, or, slt
  Branch instructions: beq, j
§4.1 Introduction

## Slide 5
논리곱
논리합

## Slide 6: Logic Design Basics (Appendix B)
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element (조합회로)
  입력 데이타를 연산해서 새로운 값을 만드는데 사용된다.
  Output = f (current input)
State (sequential) elements (순차회로)
  연산된 데이타를 저장해 두었다가 나중에 읽어내기 위해 사용된다.
  Output = f (current input, previous input)
§4.2 Logic Design Conventions

## Slide 7: Combinational circuit 은 진리표만 주어지면 만들 수 있다.

## Slide 8: Combinational Elements
AND-gate
  Y = A B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)
control

## Slide 9: 32-bit 2-to-1 MUX
=

## Slide 10: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 11: Sequential Elements
Register with write control (no read control)
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 12: Digital 회로의 동작
클락 사이클 동안(Between clock edges) 에 Combinational 회로에서 입력 신호에 대한 출력 신호를 만든다
combinational 회로의 input은 state elements의 output이다.
combinational 회로의 output은 state elements의 input이다.
clock period (clock edge 간의 간격) 은 combinational 회로의 longest delay 에 의해 정해진다.

## Slide 13: Sequential Circuit : Register (clock signal 은 생략)
a 32-bit register = 1-bit D flip flop x 32
- write signal 이 없으면 write signal 은 항상 1
- clock signal 도 있지만 (그림에서) 생략
CLK
Write = 1
32
32
…
31
1
30
31
30
1
0
0
=

## Slide 14: Sequential Circuit : Memory (clock signal 은 생략)
Instruction memory is read-only in this implementation
32
32
32
32
32

## Slide 15: Sequential Circuit : Register File (clock signal 은 생략)
32 x 32-bit registers
RegWrite =1 일 때만 레지스터의 값이 바뀌고
RegRead signal 이 없는 것은 항상 (매 클럭마다) 레지스터가 읽혀져 출력값이 된다는 뜻임
32
32
32

## Slide 16
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.
1) Build a datapath first and 2) add a control
  add, sub, and, or, slt
  lw, sw
  beq, j

## Slide 17: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
§4.3 Building a Datapath
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 18: How instructions are executed in a processor
1) Fetch instruction : instruction memory 중 PC가 가리키는 주소에서 수행할 instruction 을 프로세서로 읽어온다.
(PC 는 4만큼 자동 증가)
2) Execute instruction : 그 명령어를 수행한다.
2-1)명령어를 해석하는 동시에 Register file 에서 레지스터 값을 읽는다.
2-2) 명령어 종류에 따라 다음을 실행한다.
Arithmetic/Logic 연산 -> 결과를 레지스터에 쓴다.
Memory 주소 계산 -> data memory 에 쓴다.
-> data memory 를 읽는다 -> 결과를 레지스터에 쓴다.
Branch target address 계산 -> BTA 를 PC 에 쓰거나 쓰지 않는다.
  beq, j
  lw
  add, sub,
  and, or, slt
  sw
  add $8, $3, $4
  lw $9, 4($7)
  sw $10, 8($11)
  beq $5, $6, L
  j FN

## Slide 19
19
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.5 Two state elements are needed to store and access instructions, and an adder is needed to compute the next instruction address. The state elements are the instruction memory and the program counter. The instruction memory need only provide read access because the datapath does not write instructions. Since the instruction memory only reads, we treat it as combinational logic: the output at any time reflects the contents of the location specified by the address input, and no read control signal is needed. (We will need to write the instruction memory when we load the program; this is not hard to add, and we ignore it for simplicity.) The program counter is a 32-bit register that is written at the end of every clock cycle and thus does not need a write control signal. The adder is an ALU wired to always add its two 32-bit inputs and place the sum on its output.

## Slide 20: 1) Instruction Fetch
20
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.6 A portion of the datapath used for fetching instructions and incrementing the program counter. The fetched instruction is used by other parts of the datapath.

## Slide 21: Instruction Fetch(datapath part 1)
32-bit register
Increment by 4 for next instruction
A portion of datapath used for fetching instruction and incrementing PC
[0x00401000] add $2, $8,$9 000000 01000 01001 00010 00000 100000
000000 01000 01001 00010 00000 100000
0x00401000
0x00401004

## Slide 22: 2) Execution of Arithmetic/Logic Instructions
add $2, $8, $9
Read two register operands
Perform arithmetic/logical operation
Write a result into a destination register

## Slide 23: Datapath part 2: Execution of A/L Instructions
add $2, $8,$9 000000 01000 01001 00010 00000 100000
01000
01001
00010
0010
32
5
5
5
000000 01000 01001 00010 00000 100000
0x00000005
0x00000001
1
0x00000006
00000000
…
00000005
00000001
…
$0
$8
$9
0

## Slide 24: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 25: 3) Execution of Load/Store Instructions
lw $2, 4($8)
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 26: Part 1: Instruction Fetch
32-bit register
Increment by 4 for next instruction
[0x00402000] lw $2, 4($8) 100011 01000 00010 0000 0000 0000 0100
100011 01000 00010 0000 0000 0000 0100
0x00402000
0x00402004

## Slide 27: Datapath part 3: Execution of Data Transfer Instructions
A portion of datapath used for register access, followed by a memory address calculation, then a read or write from memory, and a write into the register file if the instruction is a load.
lw $2, 4($8) 100011 01000 00010 0000 0000 0000 0100
01000
00010
0000 0000 0000 0100
0010
0
1
10011 01000 00010 0000 0000 0000 0100
1
4

## Slide 28: part 2
4

## Slide 29: Combining part 2 and 3

## Slide 30: Role of Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 31: Part 1: Instruction Fetch

## Slide 32: Adding part 1
4

## Slide 33: 4) Execution of Branch Instructions
beq $3, $4, L
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to (PC + 4)

## Slide 34: Fetching beq instruction
4
000100 00011 00100 0000 0000 0000 0010
[0x00403000] beq $3, $4, L 000100 00011 00100 0000 0000 0000 0010
0x00403000
0x00403004

## Slide 35: part 4: Branch Instructions
Just re-routes wires
Sign-bit wire replicated
A portion of datapath used for evaluating a branch condition and computing branch target address
beq $3, $4, L 000100 00011 00100 0000 0000 0000 0010
00011
00100
0000 0000 0000 0010
0110
0
000100 00011 00100 0000 0000 0000 0010
0000 0000 0000 0000 0000 0000 0000 0010
00000000
…
00000005
00000005
00000001
…
$0
$3
$4
0x00000005
0x00000005
1
0x00000000
0x00403004
0000 0000 0000 0000 0000 0000 0000 1000
0x0040300C
Register File

## Slide 36: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 37: Adding part 4
?

## Slide 38: Full Datapath

## Slide 39: CPU Overview
Processor
Memory

## Slide 40: Datapath
Use multiplexors to stitch them together

## Slide 41: Datapath part 2: Execution of A/L Instructions
add $2, $8,$9 000000 01000 01001 00010 00000 100000
01000
01001
00010
0010
32
5
5
5
000000 01000 01001 00010 00000 100000
0x00000005
0x00000001
1
0x00000006
00000000
…
00000005
00000001
…
$0
$8
$9
1

## Slide 42: Datapath part 3: Execution of Data Transfer Instructions
lw $2, 4($8) 100011 01000 00010 0000 0000 0000 0100
01000
00010
0000 0000 0000 0100
0010
0
1
10011 01000 00010 0000 0000 0000 0100
1
4

## Slide 43: 중간고사
10/23 수 오후 8-9pm 시
강의실 배정은 공지사항에서 각자 확인할 것

## Slide 44: 중간 수업 평가 해주세요. 주관식
종합정보시스템에서 온라인 입력 주관식 1문항
10/17 목 10:00 ~ 10/27 일 24:00
강의 개선에 활용합니다.