## Slide 1
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.5 The organization of a computer, showing the five classic components. The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.

## Slide 2: CPU Overview
Processor
Memory

## Slide 3: Datapath

## Slide 4: Datapath With Control

## Slide 5
Memory
Processor

## Slide 6
Harvard Architecture vs. Von Neumann Architecture
• von Neumann Architecture
  • Same memory holds data, instructions.
  • A single set of address/data buses between CPU and memory
• Harvard Architecture
  • Separate memories for data and instructions.
  • Two sets of address/data buses between CPU and memory

## Slide 7: Roles of Instruction Fields
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 8: Execution of Arithmetic/Logic Instructions

## Slide 9
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.16 The effect of each of the seven control signals. When the 1-bit control to a two-way multiplexor is asserted, the multiplexor selects the input corresponding to 1. Otherwise, if the control is deasserted, the multiplexor selects the 0 input. Remember that the state elements all have the clock as an implicit input and that the clock is used in controlling writes. Gating the clock externally to a state element can create timing problems. (See Appendix B for further discussion of this problem.)
Meaning of Control Signals

## Slide 10: Execution of R-type (Arithmetic/Logic) instruction
add $2, $8,$9 000000 01000 01001 00010 00000 100000
01000
01001
00010
000000
100000
1
10
0
0
0
0
0
0
1
0010
(+)

## Slide 11: ALU Control
ALU used for
  R-type: F depends on funct field
  Load/Store: F = add
  Branch: F = subtract
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 12: 2단계로 ALU control 을 구현
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw(0x23) | 00 | load word | XXXXXX | add | 0010
sw(0x2b) | 00 | store word | XXXXXX | add | 0010
beq(0x04) | 01 | branch equal | XXXXXX | subtract | 0110
R-type (0x00) | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
instruction 으로부터의 input
control 회로에서 만들어지는 output

## Slide 13: 2단계로 ALU control 을 구현
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw(0x23) | 00 | load word | XXXXXX | add | 0010
sw(0x2b) | 00 | store word | XXXXXX | add | 0010
beq(0x04) | 01 | branch equal | XXXXXX | subtract | 0110
R-type (0x00) | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
instruction 으로부터의 input
control 회로에서 만들어지는 output

## Slide 14
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.13 The truth table for the 4 ALU control bits (called Operation). The inputs are the ALUOp and function code field. Only the entries for which the ALU control is asserted are shown. Some don’t-care entries have been added. For example, the ALUOp does not use the encoding 11, so the truth table can contain entries 1X and X1, rather than 10 and 01. Note that when the function field is used, the first 2 bits (F5 and F4) of these instructions are always 10, so they are don’t-care terms and are replaced with XX in the truth table.

## Slide 15: Load Instruction

## Slide 16: Execution of lw instruction
lw $2, 4($8) 100011 01000 00010 0000 0000 0000 0100
01000
00010
100011
0000 0000 0000 0100
00
0010
(+)
1
0
1
1
0
1
0
0
0x00000004

## Slide 17: 2단계로 ALU control 을 구현
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw(0x23) | 00 | load word | XXXXXX | add | 0010
sw(0x2b) | 00 | store word | XXXXXX | add | 0010
beq(0x04) | 01 | branch equal | XXXXXX | subtract | 0110
R-type (0x00) | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
instruction 으로부터의 input
control 회로에서 만들어지는 output

## Slide 18: Branch-on-Equal Instruction

## Slide 19: Execution of branch instruction
beq $3, $4, L 000100 00011 00100 0000 0000 0000 0010
000100
00011
00100
0000 0000 0000 0010
01
0110
(-)
0/1
0/1
0
X
0
X(0)
X
1
0
X
0x00000002
0x00000008
PC+4
BTA

## Slide 20: 2단계로 ALU control 을 구현
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw(0x23) | 00 | load word | XXXXXX | add | 0010
sw(0x2b) | 00 | store word | XXXXXX | add | 0010
beq(0x04) | 01 | branch equal | XXXXXX | subtract | 0110
R-type (0x00) | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
instruction 으로부터의 input
control 회로에서 만들어지는 output

## Slide 21: Control Signals

## Slide 22: Truth table for the control
Input
Output

## Slide 23: Our Simple Control Structure
All of the control logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer right away
  we use write signals along with clock to determine when to write
  (registers and memory are written at the end of the cycle)
Cycle time determined by length of the longest path

## Slide 24: Performance of Single Cycle Machines
Calculate the minimum cycle time assuming negligible delays except:
  memory (200ps), ALU and adders (100ps), register file access (50ps)

## Slide 25
Instruction class | Inst. memory | Register read | ALU operation | Data memory | Register write | total
ALU type | 200 | 50 | 100 | 0 | 50 | 400ps
Lw | 200 | 50 | 100 | 200 | 50 | 600ps
Sw | 200 | 50 | 100 | 200 |  | 550ps
Branch | 200 | 50 | 100 |  |  | 350ps
Jump | 200 |  |  |  |  | 200ps
Clock rate :

## Slide 26: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory ® register file ® ALU ® data memory ® register file
Not feasible to vary period for different instructions
We will improve performance by pipelining