## Slide 1: Pipeline Hazards
Situations that prevent starting the next instruction in the next cycle
Structural hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 2: Structural Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 3: Solution to Structural Hazards

## Slide 4: Dependencies

## Slide 5: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
pipeline stall

## Slide 6: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 7: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 8: Dependencies & Forwarding
Chapter 4 — The Processor — 8

## Slide 9: Modification to the pipeline datapath

## Slide 10: Detecting the Need to Forward (1)
Chapter 4 — The Processor — 9
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 11: Detecting the Need to Forward (2)
Chapter 4 — The Processor — 10
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 12: Forwarding Paths

## Slide 13: Meaning of ForwardA/B control signals

## Slide 14: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
add $4, $x, $x
sub $x, $4, $x
add $4, $x, $x
sub $x, $x, $4
add $4, $x, $x
xxx xx, xx, xx
sub $x, $4, $x
add $4, $x, $x
xxx xx, xx, xx
sub $x, $x, $4

## Slide 15: Double Data Hazard
Consider the sequence:
  add $10,$11,$12 and $10,$16,$13 sub $15,$10,$14
Forward from which stage?
  the most recent value
Revise MEM hazard condition
  Only forward if EX hazard condition isn’t true
ForwardA = 10
ForwardA = 01
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01

## Slide 16: Truth table of Forwarding Unit
EX/MEM.RegWrite | EX/MEM.rd=ID/EX.rs | MEM/WB.RegWrite | MEM/WB.rd=ID/EX.rs | ForwardA | Source
1 | 1 | X | X | 10 | EX/MEM
X | 0 | 1 | 1 | 01 | MEM/WB
0 | X | 1 | 1 | 01 | MEM/WB
Otherwise |  |  |  | 00 | ID/EX
EX/MEM.RegWrite | EX/MEM.rd=ID/EX.rt | MEM/WB.RegWrite | MEM/WB.rd=ID/EX.rt | ForwardB | Source
1 | 1 | X | X | 10 | EX/MEM
X | 0 | 1 | 1 | 01 | MEM/WB
0 | X | 1 | 1 | 01 | MEM/WB
Otherwise |  |  |  | 00 | ID/EX
input
output

## Slide 17: Datapath with Forwarding

## Slide 18: Solving Hazard b/w SUB & AND instructions (CC4)

## Slide 19
Solving Hazard b/w SUB,AND & OR instructions (CC5)

## Slide 20: Solving Hazard b/w AND,OR & ADD instructions (CC6)

## Slide 21: 2 Multiplexors to the 2nd input of ALU

## Slide 22: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value is not computed when needed

## Slide 23: Load-Use Data Hazard
Need to stall for one cycle

## Slide 24: Load-Use Hazard Detection
Check when an instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble
lw $2, 20($1)
and $4, $2, $5

## Slide 25: Datapath with Hazard Detection
Rs
Rt

## Slide 26: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  또 한 번 같은 명령어를 decode
  또 한 번 같은 명령어를 fetch
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 27: Truth table of Hazard Detection Unit
ID/EX.MemRead | ID/EX.rt = IF/ID.rs | ID/EX.rt = IF/ID.rt | PCWrite | IF/IDWrite | Control MUX
1 | 1 | X | 0 | 0 | 0
1 | X | 1 | 0 | 0 | 0
Otherwise |  |  | 1 | 1 | 1
lw $2, 20($1)
and $4, $2, $5
0
0
0

## Slide 28: Detecting Hazard at clock 3
0
0
0

## Slide 29: Bubble at EX stage at clock 4

## Slide 30: Bubble at MEM stage at clock 5…
01

## Slide 31: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 32: Stall/Bubble in the Pipeline
Or, more accurately…

## Slide 33: Datapath with Hazard Detection

## Slide 34: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 35: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture