## Slide 1: Control (Branch) Hazards
Branch 명령은 flow of control 을 변경한다.
  Fetch 할 다음 명령어의 주소는 branch 조건에 따라 달라진다.
Solution to branch hazard
  pipeline stall
  branch prediction
    static
      as taken
      as not taken
      상황에 따라
    dynamic

## Slide 2: Pipeline Stall on Branch Instr.
Wait until branch outcome determined before fetching next instruction

## Slide 3: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if the prediction is wrong
In MIPS pipeline
  predict branches as not taken

## Slide 4: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 5: Reducing Branch Delay
Modification of the hardware
  Target address adder in ID stage
  Register comparator in ID stage
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)
 immediate field 에 저장된 offset value
44 + 7 x 4

## Slide 6: Example: Branch Taken (CC3)
IF.Flush 가 1이면 IF/ID 의 instruction 부분에 0x00000000 (nop) 이 써짐
Branch
zero

## Slide 7: Example: Branch Taken (CC4)

## Slide 8: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect
branch not taken
one cycle stall

## Slide 9: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 10: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture