## Slide 1: 1.6 Performance

## Slide 2
Which of these airplanes has the best performance?
Airplane Passengers Range (mi) Speed (mph)
Boeing 777 375 4630 610
Boeing 747 470 4150 610
BAC/Sud Concorde 132 4000 1350
Douglas DC-8-50 146 8720 544
Which is fastest?
  In transporting a single passenger
  In transporting 450 passengers
  In transporting 130 passengers 8000 miles away

## Slide 3: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 4: Execution Time
Elapsed Time (or wall-clock time, response time)
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
  Unix command :
  %time ls
  90.7u 12.9s 2:39 65%
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program
user CPU time
system CPU time
elapsed time
user+system time
-------------------------
elapsed time

## Slide 5: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 6: Example
2 GHz 클럭의 컴퓨터 A 에서 10초에 수행되는 프로그램이 있다.
이 프로그램을 6초에 수행하는 컴퓨터를 설계하고자 한다.
클럭 속도는 얼마든지 빠르게 만들 수 있는데 이렇게 하면 CPU 다른 부분의 설계에 영향을 미쳐 같은 프로그램에 대해 A보다 1.2 배 많은 클럭 사이클이 필요하게 된다고 한다.
컴퓨터 B의 클럭 속도는 얼마로 해야 하겠는가?


## Slide 7: Example: solution

## Slide 8: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 9: # of Instructions Example
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require one, two, and three cycles (respectively). The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C. Which sequence will be faster? How much? What is the CPI for each sequence?

## Slide 10: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 11: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 12: CPI Example
Suppose we have two implementations of the same instruction set architecture (ISA). For some program, Machine A has a clock cycle time of 250 ps. and a CPI of 2.0 Machine B has a clock cycle time of 500 ps. and a CPI of 1.2 What machine is faster for this program, and by how much?
If two machines have the same ISA which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will always be identical?

## Slide 13: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 14: Amdahl's Law
Example:
"Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?" How about making it 5 times faster?
Principle: Make the common case fast

## Slide 15: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 16: Effect of Compiler Optimization
Chart: 
| none | O1 | O2 | O3
Relative Performance | 1 | 2.37 | 2.38 | 2.41
Chart: 
| none | O1 | O2 | O3
Clock Cycles | 158615 | 66990 | 66521 | 65747
Chart: 
| none | O1 | O2 | O3
Instruction count | 114938 | 37470 | 39993 | 44993
Chart: 
| none | O1 | O2 | O3
CPI | 1.38 | 1.79 | 1.66 | 1.46
Compiled with gcc for Pentium 4 under Linux