## Slide 1: 3.5 Floating Point Numbers

## Slide 2: 기말고사 일정
12/10,12,17,19

## Slide 3: Floating Point Numbers
Representation for non-integral numbers
  Including very small and very large numbers
Scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 4: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 5: IEEE Floating-Point Format
S: sign bit (0 Þ non-negative, 1 Þ negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 6: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001 Þ actual exponent = 1 – 127 = –126
  Fraction: 000…00 Þ significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110 Þ actual exponent = 254 – 127 = +127
  Fraction: 111…11 Þ significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 7: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001 Þ actual exponent = 1 – 1023 = –1022
  Fraction: 000…00 Þ significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110 Þ actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11 Þ significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 8: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 9: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 10: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.01 × 22
  = –5.0

## Slide 11: Comparison of floating point numbers
Comparison of floating point numbers:
  Compare signs
  Compare remaining part as an unsigned integer
  Example : 0.75 vs. 3.45
  (How do we compare unsigned integers?)

## Slide 12: Example : Decimal  Binary
0.75
  decimal: .75 = -3/4 = -3/22
  binary: .11 = -1.1 x 2-1
  floating point: exponent = 126 = 01111110
  IEEE single precision:
  0 01111110 100 0000 0000 0000 0000 0000
3.45
= (-1)0x(1.101110011001100…)x21
0 10000000 101 1100 1100 1100 1100 1101

## Slide 13: Denormal Numbers
Exponent = 000...0 Þ hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 14: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 15: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 16: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 17: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 18: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 19: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212 Þ 10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 20: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.110 Þ 1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve Þ –ve
  –1.1102 × 2–3 = –0.21875

## Slide 21: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP « integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 22: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
  (pseudoinstructions l.s, l.d, s.s, s.d)
    e.g., ldc1 $f8, 32($sp)

## Slide 23: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le)
  Sets or clears FP condition bit
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel

## Slide 24: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, 0($gp) lwc2 $f17, 4($gp) div.s $f16, $f16, $f17 lwc1 $f17, 8($gp) sub.s $f17, $f12, $f17 mul.s $f0, $f16, $f17 jr $ra

## Slide 25
.data 0x10008000
f5: .float 5.0
.float 9.0
.float 32.0
.float 70.0
.text
.globl main
main:
addi $sp, $sp, -4
sw $ra, 0($sp)
lwc1 $f12, 12($gp)
jal f2c
lw $ra, 0($sp)
addi $sp, $sp, 4
jr $ra
f2c:
lwc1 $f16, 0($gp)
lwc1 $f17, 4($gp)
div.s $f16, $f16, $f17
lwc1 $f17, 8($gp)
sub.s $f17, $f12, $f17
mul.s $f0, $f16, $f17
jr $ra

## Slide 26: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 27: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism