## Slide 1: Virtual Memory

## Slide 2: Analogy between cache and VM
 | Cache | VM
Upper level memory | Cache | Main memory
Lower level memory | Main memory | Secondary Storage
Unit of transfer | Block (32~128B) | Page (4~16 KB)
Upper level memory organization | Direct-mapped or set-associative | Fully associative
Replacement scheme | Random | LRU
Write scheme | Write-through or write-back | Write-back
Miss penalty | Relatively low | Relatively large

## Slide 3: Virtual Memory
Main memory can act as a cache for the secondary storage (disk)
Advantages:
  illusion of having more physical memory
  program relocation
  protection
upper level
memory
lower level
memory
program uses
virtual address

## Slide 4: Pages: virtual memory blocks
Page faults: the data is not in memory, retrieve it from disk
  huge miss penalty, thus pages should be fairly large (e.g., 4~16KB)
  reducing page faults is important (LRU is worth the price)
  can handle the faults in software instead of hardware
  using write-through is too expensive so we use writeback
address translation

## Slide 5: Page Tables :
: direct-mapped
: fully associative

## Slide 6: Address translation
Where is the page table?
0000 0000 0000 0000 0100 0000 0000 1000
01 0000 0000 0000 0000
01 0000 0000 0000 0000 0000 0000 1000
4

## Slide 7: What is memory address?
메모리에 저장된 것은 2진수 형태의 data 들 (bit 들의 모임) 이고,
이 수많은 bits 중 특정한 bits 를 지칭하기 위한 일련번호가 주소이며
다시 말하지만, 주소(index)는 메모리(cache)에 저장된 것이 아닙니다!!!
00100000
01011100
10111110
00001100
01001111
00000000
10101101
11110000
8B=64bits memory
word addressing
byte addressing
0
1
000
001
010
011
100
101
110
111
Mem[1112]

## Slide 8: Making Address Translation Fast
A cache for address translations: translation lookaside buffer (TLB)
Typical values: 16-512 entries,
miss-rate: 0.01% - 1%
miss-penalty: 10 – 100 cycles
virtual address : 0000 0000 0000 0000 0001 0000 0000 1000
0000 0000 0000 0000 0001
1
0000 0000 0000 0000 0101
0000 0000 0000 0000 0001
0000 0000 0000 0000 0101
physical address :
0000 0000 0000 0000 0101 0000 0000 1000

## Slide 9: Virtual memory + cache example
0000 0011 0000 0000 0001 0000 1100 0100
0000 0011 0000 0000 0001 0000 1000 0000 1000
0000 1000 0000 0000 1000 0000 1100 0100
0000 1000 0000 0000 10 00 0000 11 00 01 00
3
0000 1000 0000 0000 10
0x030
0x031
0x032
0x03F
page table
main memory
secondary storage