## Slide 1: Chapter 1
Computer Abstractions and Technology

## Slide 2: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity
§1.5 Technologies for Building Processors and Memory

## Slide 3: The First Electronic Computers
1946 ENIAC with 18,000 vacuum tubes, in UPenn

## Slide 4: The First Commercial Computer in U.S.
in 1951, UNIVAC is sold for $1M

## Slide 5: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive : 4차 산업혁명?
§1.1 Introduction

## Slide 6: Moore’s law
An observation made by Gordon Moore, co-founder of Intel
“The number of transistors in an IC(Integrated Circuit) doubles every year.” in1965 paper
“The number of transistors in an IC doubles every 18~24 months.” (updated in 1975)

## Slide 7
By Steve Jurvetson - https://www.flickr.com/photos/jurvetson/31409423572/, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=55002144

## Slide 8
By Wgsimon - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=15193542

## Slide 10
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.1 The 2X vs. 10Y bytes ambiguity was resolved by adding a binary notation for all the common size terms. In the last column we note how much larger the binary term is than its corresponding decimal term, which is compounded as we head down the chart. These prefixes work for bits as well as bytes, so gigabit (Gb) is 109 bits while gibibits (Gib) is 230 bits.

## Slide 14: Classes of Computers
Personal computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized

## Slide 15: Classes of Computers
Supercomputers
  High-end scientific and engineering calculations
  Highest capability but represent a small fraction of the overall computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints

## Slide 16: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google

## Slide 17: What is “Computer Architecture”?
Computer
Architecture
Coordination of many
levels (layers) of abstraction
I/O system
Processor
Compiler
Operating
System
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 18: Instruction Set Architecture
A very important abstraction
  interface between hardware and low-level software
  standardizes set of instructions, their operations and machine language representations.
  advantage: different implementations of the same architecture
  disadvantage: sometimes prevents using new innovations (Compatibility issue)
RISC (Reduced Instruction Set Computer) vs. CISC (Complex Instruction Set Computer)

## Slide 19: Power Trends
In CMOS IC technology
§1.7 The Power Wall
×1000
×30
5V → 1V

## Slide 20: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 21: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization